Experimental Loop Antenna for 40m
Colin Berry
M0GXV

---
Contents
- What is a 'magnetic' loop?
- Why build one?
- But...
- Practical project
- Theory
- Modelling Techniques
- Performance
- Going further

---
What is a 'Magnetic' Loop?
- Small enough to be a 'circuit'
- Big enough to have a phase difference
- Capacitor tuned
- Loosely coupled
- Strong magnetic near-field
Dipole
Loop
Near field

---
Why Build One?
- Experimentation / learning
- Indoor / hidden
- Scrapheap challenge
- Compact and portable
- No RF earth needed
- Local E - qrm insensitivity
- Multi-band tunable
- Re-orientable

---
But...
- Difficult to tune / narrow bandwidth
- Tuned at antenna, not ATU
- Low efficiency
- Local B - qrm sensitivity
- High local B field - interference
- Plumbing skills needed
- Set-up equipment required
- High power needs an expensive capacitor

---
Practical Project
- Pipework
- Capacitor
- Coupling
- Mounting
- Tuning

---
Theory
- Radiation and near field
- Efficiency
- Inductor
- Capacitor
- Coupling

---
Electric/Magnetic Fields
Jefimenko's equations

---
Equivalent Model
- Anti-phase dipoles – same 'area' & phase
- Receives changing magnetic field
Current
observation
r
Current
l

---
Local magnetic field strengths
Distance

---
Efficiency
- Radiation: Charge acceleration * phase difference factor
- Radiation resistance = (power radiated) / current²
  -  (radius/wavelength)⁴
  - Compare with short dipole,  (length/wavelength)²
- Extra loss resistance from:
  - Skin resistance
  - Dielectric (if any)
  - Connections
  - Near field absorption
- Efficiency = radiation resistance / total resistance
- Q, bandwidth and efficiency are related

---
Bandwidth, Q and Efficiency
- Unloaded Q = reactance / resistance
- When matched receiver connected, loaded Q is half this
- Receiver bandwidth between -3dB points = frequency / loaded Q
- Pure radiation resistance: 0.015Ω
  - unloaded Q 11000, SWR < 1.5 over 0.3 kHz
- Efficiency reduced by actual Q / pure Q

---
Theory - Inductor
- Inductance of a loop:
- Skin depth (microns):
- At 7MHz : 150j Ω + 0.06 Ω + joints
  - For 15mm diameter copper pipe
- Can add extra turns for low frequency use

---
Theory - Capacitor
- Parallel plate capacitance:
- LDPE dielectric:
  - Relative permittivity 2.2
  - Loss resistance: reactance x 0.0003 (PVC is 0.01)
- 0.3mm “picture frame” spacer adds ~ 50% to capacitance
- Loop has some capacitance too

---
Theory – Coupling
- Separate loop acts as transformer
- Adjust to match loop resistance → 50Ω
- Series capacitor neutralises self inductance
  - Used length of microphone coax cable
  - Alternative to using ATU
- Alternatives
  - Tiny capacitor, off-tuning
  - Gamma match

---
Tuning
- Neutralise coupling inductance
- Tune main loop
  - Course tuning – grid dip oscillator or antenna analyser
  - Fine tuning – Tx + absoption wavemeter, or antenna analyser
- Adjust coupling loop spacing or ATU to match to transmitter
- Measure bandwidth, deduce Q
- Determine maximum drive power (and ERP)

---
Modelling Techniques
- Equivalent circuit – coupled resonators
- Standard loop calculations
  aa5tb_loop_v1.22a
- Complex number maths in spreadsheets
  SWR vs bandwidth
  C:\Users\Colin\Documents\magloop mutual coupling.ods
- NEC simulation

---
Performance
- Receiver bandwidth around 25kHz
  - Loss resistance 0.5Ω
  - Effective unloaded Q around 500
- Efficiency 5% (-13dB vs perfect dipole)
- SWR < 1.5 over 10kHz
- Power limit? Predicted 25W input, 1W ERP
- On 40m : SSB QSO to GB1RR Nottingham

---
Going Further
- Next steps in project
  - Additional variable capacitor for fine tuning
  - Mount on pole
  - Investigations into unexplained losses
- Alternative approaches
  - Different loop materials / number of turns / thickness
  - High voltage variable capacitor with motor drive
    - Vacuum capacitor is best but expensive
- Commercial loops
  - MFJ 1788X at £530
  - Www.wimo.com - up to €1500
- Constructional articles
  - RadCom December 2015
  - many photos and articles on internet